## Slide 1: STM32MP1 CommSTSDK Python Package
SRA Agrate – Apr 2020

## Slide 2: Summary
Rationale
The CommSTSDK Python3 package was developed with the aim of tackling and reducing the usage complexity of inter-processors communications in the ST-MP1 AMP MPU.
The main objective of this package is to allow a Python application developer to easily exploit the MPU AMP architecture by means of facilitating the communications among the Master MPU (aka A7), and the Slave MCU (aka M4).
The above objective is reached by means of:
  Filling the gap between the OpenAMP RpMsg and Python pyserial library
  Creating a C Linux shared object library connecting the librpmsg_sdb_sdk.so kernel object to the new Python plugin

## Slide 3: Summary
Plugin Internals
The CommSTSDK Python3 plugin is divided in three parts:
The “CommAPI” python class to easy the exchange of short ASCII msg/cmds between the A7 Master and M4 Slave processors
The “RpmsgSdbAPI” python class to easy the exchange of long Shared Data Buffers (SDB) from M4 Slave to A7 Master processor.
The “libsdbsdk.so” shared object library providing the userland interface to the “Stm32_rpmsg_sdb.ko” kernel object. This shared library is an helper backend for the “RpmsgSdbAPI” Python Class to access the shared memory

## Slide 4: CommSTSDK SW Layers
commsdk
Python application
A7
(Master)
M4
(Slave)
STM32Cube
SDB Data Producer FW
OpenAmp/Virtual UART
pyserial
OpenAMP
RpMsg
Stm32_rpmsg_sdb.ko
CommAPI
/dev/ttyRPMSG0
Sdbsdk.so
RpmsgSdbAPI
SDB buffers/Mmap
Legenda:
Py plugin layers
Application layers
Distro/Fw layers
Hw layers
Logical communication

## Slide 5: Use Cases Diagram
commsdk
Send (“cmd”) to M4
Recv (“answ”) from M4
Ntfy (“ntfy”) from M4
Use case 1: Send/Recv Sync/Async ASCII cmds/answs/ntfy to/from M4
Init commsdk (Vcom, m4fw)

## Slide 6: Use Cases Diagram
commsdk
Send (“cmd”) to M4
Recv (“answ”) from M4
Ntfy (“ntfy”) from M4
Use case 2: Recv Async Shared Data Buffer from M4
Py_sdbsdk
Ntfy (SDB) from M4
Init commsdk (Vcom, m4fw)
Init py_sdbsdk ()

## Slide 7: Sequence Diagram (Use Case 1)
User App
CommAPI
Pyserial
M4_asw_listener
Obj inst(vCom0,M4fw)
Obj1 inst()
M4_ntfy_listener
Obj2 inst(vCom1)
M4Fw
Add_answ_listener(Obj1)
Add_ntfy_listener(Obj2)
Cmd_get(“cmd”)
Start M4Fw
processing
vCom0 “cmd”
On_m4_answ_cb()
On_m4_ntfy_cb()
vCom1 “ntfy”
vCom0 “answ”

## Slide 8: Sequence Diagram (Use Case 2)
User App
CommAPI
Pyserial
RpmsgSdbAPI
Obj inst(vCom0,M4fw)
Obj1 inst()
M4_sdb_listener
M4Fw
Add_sdb_buff_listener(Obj2)
Start M4Fw
vCom0 “r”
Init_sdb(sdbsz, n)
Start_sdb_receiver()
Obj2 inst()
Cmd_set(“r”)
Sdbsdk.so
stm32sdb.ko
Cmd_set(“S002M”,0)
vCom0 “S002M”
Run M4 Fw
Set M4 Fw sampling rate
Mmap sdb buffs
On_m4_sdb_rx(psdb, sdblen)
Cmd_set(“Exit”,0)
Send sdb

## Slide 9: API usage semantics (Use Case 1)
Cmd_set/get(msg, tmo)
tmo = 0 or tmo = -1
Synchronous blocking call:
Blocks until answer/ack arrives from M4
tmo > 0
Asynchronous non blocking call:
Return immediately. Answer/ack, if any, arrives from M4 through “CommAPIAnswersListener” interface call back
Only one outstanding cmd at time is allowed.

## Slide 10: Dependencies
The kernel object stm32_rpmsg_sdb.ko must be available on the MP1-DK2 distribution used. Also the associated M4 Slave Fw must be present to run the plugin. Both are available into the bitbacke layer “meta-st-stm32mpu-app-logicanaliser”
Despite it is written in Python the commsdk plugin can be run only on MP1-DK2 boards because it relies on the specific subtending SoC architecture and Sw (eg. OpenAmp, SMP Soc, Shared Memory, STLinux, M4Fw etc.).
Any modification to the Python plugin should be done on the MP1-DK2 board as the included makefile, for the C part compilation, do not provide cross compilation. This imply the availability on the MP1-DK2 board of the “built-essentials” and Git
The Shared Data Buffer exchange (aka sdb) in the current pgin version is mono-directional from the M4 (Slave processor acting as a producer) to the A7 (Master processor acting as a consumer)